## Slide 1: UH-60A Airloads Wind Tunnel Data Update
Tom Norman
Airloads Workshop
Feb 28 – Mar 1, 2013

## Slide 2: Outline
Current NASA Activities
Recent/Upcoming Airloads Publications
Data Storage Uncertainties
Recent Test Information
  Section moment integration error
  Mean lag comparisons with analysis

## Slide 3: Current NASA Activities
Continuing data evaluation/reduction efforts for rotor data, Blade Displacement, PIV, and RBOS
  Internal Govt meeting held Dec. 2012 to discuss data reduction status and future plans
  Still have some work to do on data reduction process – work with CFD analysts providing valuable insights
  Current goal to provide validated, accessible results for key points by early fall
Continuing evaluation of slowed-rotor data with CAMRAD
Continuing CFD validation efforts with both OVERFLOW and FUN3D

## Slide 4: NASA Activities - OVERFLOW
Completed AIAA paper showing effects of wind tunnel and LRTA models on rotor loads and performance (Chang)
Continuing modeling in-board blade shank for better performance calculations (Romander/Lim)
Continuing comparisons between CFD and blade deflection measurements (Romander)
Performing computations for comparison with PIV measurements (Ahmad)

## Slide 5: NASA Activities - FUN3D
Completed coupling of hi-res CAMRAD and RCAS with FUN3D
Completing thrust- and speed-sweep computations
  With and without LRTA
  Free air vs tunnel
  Trim tab vs no trim tab
Performed computations for blade deflection pt (R42P60)
  Compared airloads and pressures
  Deflections yet to be examined

## Slide 6: Recent/Upcoming Airloads Publications
January AIAA Mtg (2)
  “Analysis of the UH-60A Rotor Loads Using Wind Tunnel Data”, Marpu et al
  “Airloads Correlation of the UH- 60A Rotor Inside the 40- by 80- Foot Wind Tunnel”, Chang et al
AHS Forum (3)
  “Wind Tunnel Measurements of the Wake of a Full-Scale UH-60A Rotor in Forward Flight”, Wadcock et al
  “Retroreflective Background Oriented Schlieren of Tip Vortex Visualization and Mapping for UH-60 Airloads”, Schairer et al
  “FUN3D Airload Predictions for the Full-Scale UH-60A Airloads Rotor in a Wind Tunnel”, Lee-Rausch et al
Summer AIAA Mtg (1)
  “Comparison of Computed and Measured Vortex Evolution for a UH-60A Rotor in Forward Flight”, Ahmad et al

## Slide 7: Data Storage Uncertainties
Selected wind tunnel data available to Workshop participants since Nov 2011 through NASA’s NSC Knowledge Now website
Nov 2012 hack of NSCKN site prompted NASA to alter its security approach
  Starting April 2013, all NSCKN users must have a “NASA Identity” in order to access site
  NASA Identify typically requires formal application, Govt background check, IT security training, etc
Looking for alternative method for data distribution (or streamlined NSCKN process)
  Similar issue for distribution sites for OVERLOW and FUN3D

## Slide 8: Section Moment Integration Error
Numerical integration scheme for wind tunnel section loads is equivalent to that used for UH-60A Airloads flight test
  2nd order integration of pressures using mapped coordinates
Although integrated pressures can theoretically be absolute or gage (p-pstatic), it was recently determined that choice can affect mean section moments
  Differences noted when xducer locations on top and bottom surfaces are different
  Magnitude of differences dependent on location/magnitude of working xducers as well as magnitude of static pressure
  Does not affect normal or chord forces
  Numerical integration errors minimized if use gage pressure
Wind tunnel data reduction used absolute pressures for integration (flight test used gage)
  Will re-reduce all WT data using gage pressures for best results

## Slide 9: Section Moment Integration Error
  PM differences are typically small
  Example with largest difference shown (R52P15, r/R=.99)

## Slide 10: Mean Lag Comparisons
Two independent systems (crabarm, laser) used to measure blade root motion during WT test
Test data showed blade to blade and method to method differences especially for the mean
  Have identified a number of possible causes for the differences (amplifier drift, offsets, RPM/CF effects)
  Still evaluating which corrections to apply
    Working with analysis, BD, and PIV data to help guide decision

## Slide 11: Mean Lag Comparisons
Measured vs Corrected Mean Lag Angle for Thrust Sweep
  Reduced scatter (note: corrections are preliminary)

## Slide 12: Mean Lag Comparisons
Corrected Mean Lag vs Predictions for Thrust Sweep
  Predictions consistently show greater lag than measurements

## Slide 13: Mean Lag Comparisons
Delta Mean Lag (Predictions – Measured)
  Relatively constant offset up to high thrust
  Will investigate to determine if this is experimental or analytical error

## Slide 14: SignOffPage
Notes: NASA Presentation Sign-Off Page